## Slide 1
REAM-R-KABLE
FIBERS
Paper and Pulp Industry
Industrial Plant Engineering
PROFME 105
Pangasinan State University
Urdaneta City Campus · College of Engineering and Architecture
Prepared by:
DELA CRUZ, JHAN RAYVEN D.
BSME 4A
Submitted to:
ENGR. MARFEL D. ROSARIO
Instructor
A.Y. 2025–2026 | May 2026
1 of 18

## Slide 2
Company Profile
2 / 18
About REAM-R-KABLE FIBERS
Location: Barangay Ciudad Real, San Jose del Monte, Bulacan
"REAM" (unit of paper) + "FIBER" (foundation of product) = REMARKABLE
VISION
To be the premier, most technologically advanced and environmentally
remarkable pulp and paper mill in Southeast Asia.
MISSION
• Deliver Excellence — high-grade paper exceeding global standards
• Champion Sustainability — water recycling; wastepaper as raw material
• Empower Community — high-value technical jobs in Bulacan
• Drive Innovation — modern engineering in pulping and refining
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 3
Introduction
3 / 18
Paper, Pulp & the Philippine Industry
PAPER — wood fibers reduced to pulp, formed into a mat, compressed, dried
PULP — fibrous material from wood/non-wood via chemical or mechanical process
Paper Grades:
• Printing & Writing (bond paper, notebooks)
• Newsprint (newspapers)
• Corrugating / Containerboard (linerboard, fluting)
• Tissue & Sanitary Papers
• Specialty (art paper, construction board)
Philippine Context:
• PICOP Resources Inc. (only integrated mill) ceased operations in 2010
• Industry now relies PRIMARILY on recycled wastepaper
• Wastepaper = 19% of total municipal solid waste in PH
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 4
Plant Location
4 / 18
San Jose Del Monte (SJDM), Bulacan
~42 km from Metro Manila | Landlocked component city
3 national roads | 4 provincial roads | 402 city roads | 15 bridges
Why SJDM?
• Proximity to Metro Manila — highest wastepaper source density
• Near Region 3 (Central Luzon) — rice straw, bagasse, bamboo supply
• Access to NAIA, Clark, Subic airports and major seaports
• Inside established industrial cluster of Central Luzon
• Bulacan Province: 279,610 ha | Cities: Malolos, Meycauayan, SJDM
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 5
Hazard Assessment
5 / 18
Why SJDM is Safe for Industrial Investment
FLOODING ➜ LOW RISK
Eastern location; away from coastal lowlands and river floodplains
STORM SURGE ➜ ZERO RISK
Inland position; surge risk confined to coastal municipalities only
LIQUEFACTION ➜ ZERO RISK
Stable bedrock / thick soil — WHITE ZONE on hazard map
LANDSLIDE (Earthquake) ➜ VERY LOW RISK
Urbanized flatland; away from Sierra Madre unstable slopes
SJDM falls in white/yellow zones across ALL FOUR hazard maps
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 6
Raw Materials
6 / 18
Industry Inputs
A. VIRGIN / WOOD PULP
Softwood (Pine, Spruce) — long fibers — strength for printing/writing paper
Hardwood (Eucalyptus, Birch) — short fibers — improves bulk and opacity
B. NON-WOOD PULP
Sources: Abaca, banana, rice straw, wheat straw, bagasse, bamboo
Abaca pulp — exceptional strength; key Philippine export commodity
C. RECYCLED WASTEPAPER (Primary Source in Philippines)
Processed via deinking + fiber separation
Reduces waste, conserves resources, lowers GHG emissions
Supplemented by imported virgin pulp when quality demands it
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 7
Chemicals & Additives
7 / 18
Key Chemicals Used in Production
PULPING CHEMICALS
Caustic Soda NaOH — breaks down wood chips into pulp
Sodium Sulfide Na2S — Kraft cooking liquor; dissolves lignin
BLEACHING AGENTS
Chlorine Dioxide ClO2 — high-level whiteness bleaching
Hydrogen Peroxide H2O2 — eco-friendly brightening agent
Sodium Hypochlorite — wastepaper pulp brightness improvement
Sodium Hydrosulfite — mechanical pulp brightening
PAPERMAKING ADDITIVES
Fillers (clay, CaCO3) — opacity, brightness, printability
Sizing agents (starch, rosin) — ink/water resistance
Retention aids, strength agents, slime control, antifoam, dyes
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 8
5 Design Constraints
8 / 18
Engineering Boundaries of the Plant
1 ENVIRONMENTAL & REGULATORY
Effluent: BOD, COD, TSS, pH strictly controlled before discharge
Air: scrubbers for total reduced sulfur (TRS) and particulate matter
2 RAW MATERIAL & FIBER
De-inking and contaminant-removal systems for recycled fiber
Large chip/bale storage areas for uninterrupted supply
3 ENERGY & UTILITY
Co-generation (CHP) target — plant aims to be energy self-sufficient
4 TECHNICAL & PROCESS
Kraft pulping + ECF/TCF bleaching (no elemental chlorine)
Duplex stainless steel / titanium for corrosion resistance
5 SITE & GEOGRAPHICAL
Near water source for intake/discharge; proximity to ports & highways
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 9
Process Flow Diagram
9 / 18
End-to-End Manufacturing Process
RAW MATERIAL PREPARATION
Debarking ➜ Log Cutting ➜ Chipping ➜ Screening ➜ Storage
↓
PULPING (choose method based on raw material)
Chemical Pulping (Kraft) | Mechanical Pulping | Wastepaper Pulping
↓
WASHING ➜ SCREENING ➜ CLEANING
↓
BLEACHING
↓
STOCK / PULP PREPARATION
Beating ➜ Blending ➜ Fillers + Sizing + Chemicals
↓
PAPERMAKING STAGE
Headbox ➜ Wire ➜ Press ➜ Dryer ➜ Size Press ➜ Calendar ➜ Reel
↓
FINISHED PRODUCT (Jumbo rolls, trimmed, shipped)
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 10
Pulping Methods
10 / 18
Three Methods Used in the Plant
METHOD 1 — CHEMICAL PULPING (KRAFT PROCESS)
Wood chips + White Liquor (NaOH + Na2S) in digester at ~160°C / 10 atm
Cellulose fibers separated from lignin; black liquor → recovery boiler
METHOD 2 — MECHANICAL PULPING
Twin rotating disk refiner physically grinds chips into fibers
Higher yield, lower strength; retains most lignin
Bleached with sodium hydrosulfite or hydrogen peroxide
METHOD 3 — WASTEPAPER PULPING
Hydrapulper: 3–5% concentration, 30–60 min mechanical agitation
Foreign objects removed by screens and cleaners (cleaners, reject separator)
Deinking: ink removed using alkali + surface-active agents
Bleaching to achieve 55–75% target brightness
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 11
Stock Preparation
11 / 18
Preparing Pulp Before Papermaking
1. BEATING
Disk refiner swells fibers; improves flexibility and surface area
More inter-fiber bonding points = stronger sheet formation
2. BLENDING
Recycles broke (trim and defective paper from production)
Blends raw materials + recovered white water from wire section
3. ADDITION OF FILLERS, SIZING AGENTS & CHEMICALS
Fillers (clay, CaCO3) — opacity, brightness, smoothness
Sizing agents (starch) — ink and water resistance
Retention aids — reduce fiber loss in wire section
Strengthening agents — improve wet and dry sheet strength
Slime control / antifoaming / dyes — added as process requires
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 12
Papermaking Stage
12 / 18
From Pulp Slurry to Finished Paper
1. HEADBOX — distributes fiber-water slurry uniformly across wire width
2. WIRE SECTION — fibers settle into mat; water drains away; sheet forms
3. PRESS SECTION — rollers + felt cloth; mechanical dewatering;
increases strength and improves surface quality
4. DRYER SECTION — steam-heated cylinders; reduces moisture to 6–10%
5. SIZE PRESS — applies starch for water resistance + surface strength
6. CALENDERING — steel roller stack; smooths surface, adds gloss,
ensures uniform sheet thickness
7. POPE REEL — winds paper into large jumbo rolls
8. REWINDER — trims and cuts jumbo rolls to sellable widths
removes defective sections; final product shipped
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 13
Key Equipment
13 / 18
Major Machinery & Specifications
RAW MATERIAL HANDLING
Roller Wood Debarker 5–18 T/H | 95% peeling rate
Bale Breaker 100–900 TPD | Dual motor drive
Round Silo Chip Storage Up to 42 m diameter
PULPING
Hydrapulper 1–102 m³ | Concentration 2–15%
Displacement Pulp Digester 110–400 m³ | 0.9–1.2 MPa
Double Disc Refiner (PM20) Max motor 315–1,800 kW
Flotation Deinking Cell Ink removal rate 0.25–0.3; 15–150 T/D
PAPERMAKING MACHINE
Headbox / Wire / Press / Dryer / Size Press / Calendar / Reel
Trim width: up to 6,600 mm | Speed: up to 2,200 m/min
Capacity: up to 1,000 TPD | GSM range: 13–500 g/m²
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 14
Manpower
14 / 18
80 Total Personnel — Priority Hiring from SJDM & Bulacan
Top Management ................ 4
Supply Chain & Logistics ...... 11
Operating Personnel (Mill) .... 19
Quality Control & Assurance ... 4
Maintenance & Engineering ..... 8
Packaging ..................... 9
EHS & Security ................ 6
Sales & Marketing ............. 7
Human Resource Administration . 7
Finance & Accounting .......... 5
──────────────────────────────────
TOTAL ......................... 80
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 15
Industry Context
15 / 18
Existing Major Paper Mills — Central Luzon
United Pulp & Paper Corp. Calumpit, Bulacan
Products: Corrugating medium, test liner
Capacity: 230,000 MT / year
Trust International Paper Corp. Mabalacat, Pampanga
Products: Newsprint, printing & writing paper
Capacity: 230,000 MT / year
Bataan 2020 Inc. Samal, Bataan
Products: Printing/writing, newsprint, tissue
Capacity: 73,000 MT / year
Container Corp. of the Philippines Quezon City
Products: Corrugating medium, chipboard
Capacity: 89,000 MT / year
SJDM sits at the center of this cluster — shared labor, suppliers & logistics
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 16
Design Computations
16 / 18
Key Calculations Summary
MASS BALANCE (Target: 1,200 kg finished paper / hour)
Dry fiber required ~1,333 kg / hr
Process water required ~25,333 kg / hr
Total pulp slurry input ~26,667 kg / hr
Water evaporated at dryer 1,800 kg / hr
PAPERMAKING MACHINE PARAMETERS
Machine speed: 200 m/min | Deckle: 3.2 m | GSM: 50
Final dryness: 95% | Dryer inlet dryness: 38%
Wire length: ~27.09 m | Size press: max 250 rpm
PIPING MATERIAL SELECTION
Kraft / Sulfite pulp ➜ Copper pipe
Mechanical / Groundwood ➜ PVC pipe
Long-fiber kraft (never dried) ➜ Stainless Steel / PVC
Soda pulp ➜ Steel pipe
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 17
Conclusion
17 / 18
Summary of Key Findings
✔ Location: SJDM, Bulacan — strategic, low-hazard, logistically superior
✔ Raw Material: Recycled wastepaper (primary) + imported virgin pulp
✔ Three Pulping Methods: Kraft Chemical, Mechanical, Wastepaper
✔ Five Design Constraints fully addressed:
Environmental, Raw Material, Energy, Technical, Site
✔ Total Workforce: 80 personnel
Priority hiring: local community of SJDM and Bulacan Province
✔ Natural hazard safe: flood, storm surge, liquefaction, landslide
OUR VISION
To be the premier, most technologically advanced, and environmentally
REMARKABLE pulp and paper mill in Southeast Asia.
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026

## Slide 18
References
18 / 18
Sources & Citations
AGICO Paper. (n.d.). Pulp mill machinery & paper making equipment.
https://agicopaper.com/
Andritz. (n.d.). KPR paper capabilities brochure.
Bureau of Energy Efficiency. (n.d.). Best practice manual: Fluid piping systems.
Golden Paper Group. (n.d.). Raw materials for paper making guide.
Paper Mill Machine. (n.d.). Pulp mill section equipment catalogue.
https://papermillmachine.com/
Provincial Government of Bulacan. (2010). PDPFP 2010–2030.
Sarkar, S. (n.d.). Headbox calculations. Scribd.
DAV University. (n.d.). MEC250-POM: Plant location and layout.
JSS College of Arts. (2023). Department file — Paper Industry Overview.
Landmark University. (n.d.). GEC524: Plant Layout.
REAM-R-KABLE FIBERS | Paper and Pulp Industry | BSME 4A | A.Y. 2025–2026